## Slide 1
The Essentials of Physical Design (RTL to GDSII)
Transforming Logic into Silicon
Presented By
K.K.SAI KUMAR

## Slide 2
Contents
Introduction to PD
Physical Design flow overview
Synopsys EDA Tool overview
Raven Wrapper Project overview
      Floorplanning
      powerplanning
      Placement
      CTS
      Routing
      Filler Insertion

## Slide 3
INTRODUCTION TO PD
Physical design is the stage in the VLSI (Very Large Scale Integration) design flow where the abstract logical circuit (netlist) is transformed into a geometrical layout (GDSII)that can be fabricated on silicon.
Logical design → Blueprint (schematics, netlist).
Physical design → Actual construction (placement of transistors, wires, blocks).
The Goal: To ensure the chip meets PPA targets:
* Power: Minimize leakage and switching power.
* Performance: Meet timing requirements (Setup/Hold).
* Area: Minimize the silicon footprint to reduce cost.
Tools Used- EDA Tools like Synopsys ICC2, Cadence Innovus, Mentor Graphics Calibre. - These are automate placement, routing, and verification.

## Slide 4
Physical Design flow overview
The RTL-to-GDSII
Physical Design Flow(Synopsys ICC2 Based)
Design Initialization
* Inputs: Verilog Netlist, SDC (Constraints), UPF (Power), Libraries (NDM/DB).
* Floorplanning
* Defining chip boundary, I/O pin placement, and Macro (SRAM) placement.
* Power Planning
* Creating the VDD/VSS mesh, rings, and stripes to minimize IR Drop.
* Placement
* Standard cell positioning and timing-driven optimization.
* Clock Tree Synthesis (CTS)
* Clock distribution, skew balancing, and buffer insertion.
* Routing
* Global and Detailed routing of all signal nets.
* Physical Verification & Sign-off
* DRC, LVS, and STA (Static Timing Analysis).

## Slide 5
Synopsys EDA Tool overview
Stage | Synopsys Tool | Primary Function
Synthesis | Design Compiler (DC) | RTL code Gate-level Netlist
Floorplanning | IC Compiler II | Die area, Macro placement, I/O pads
Placement | IC Compiler II | Standard cell positioning & optimization
CTS | IC Compiler II | Clock tree building (skew/latency control)
Routing | IC Compiler II | Final metal interconnects
Extraction | StarRC | Capturing wire resistance/capacitance
Sign-off STA | PrimeTime | Final timing check before manufacturing
Verification | IC Validator | Final physical rule check (DRC/LVS)
Stage | Synopsys Tool | Primary Function
Synthesis | Design Compiler (DC) | 
Floorplanning | IC Compiler II | Die area, Macro placement, I/O pads
Placement | IC Compiler II | Standard cell positioning & optimization
CTS | IC Compiler II | Clock tree building (skew/latency control)
Routing | IC Compiler II | Final metal interconnects
Extraction | StarRC | Capturing wire resistance/capacitance
Sign-off STA | PrimeTime | Final timing check before manufacturing
Verification | IC Validator | Final physical rule check (DRC/LVS)

## Slide 6
Raven Wrapper Project overview
Raven_wrapper is a design block for synthesis, place-and-route, and testing- Ensures compatibility with 45nm technology and multi-clocks.
Mode (func) → This suggests the wrapper is configured in functional mode (normal operation), as opposed to test/debug modes.-
Tech (45nm) → The design is targeted for a 45 nanometer technology node. This defines transistor size, power, and performance characteristics.-
Clocks (3 clocks) → The design uses three separate clock domains. Multiple clocks are common in complex chips to handle different subsystems.-
10 (Layers) → Likely refers to 10 metal layers available in the process technology for routing interconnects.
The Voltages → VDD & VSS
The Physical Cell → Filler Cell

## Slide 7
FLOOR PLANNING
Inputs for floorplanning
Netlist (.v) → Logical connectivity of the design.
Technology file (.techlef) → Process-specific rules.
Timing libraries (.lib) → Timing characteristics of cells.
Physical libraries (.lef) → Cell dimensions and layout info.
Constraints (.sdc) → Timing and design constraints.
TLU+ → Parasitic information for RC extraction.

## Slide 8
CHECKS
Die/Core Area Size
Macro placement
I/O pad placement
Errors
Placement Congestion
Orientation of macros
Misalignment of macros
FLOOR PLANNING

## Slide 9
POWER PLANNING
Creating the VDD/VSS mesh, rings, and stripes to minimize IR Drop.
Power Mesh: Horizontal and Vertical stripes using higher metal layers. Connecting VDD and VSS pins of standard cells to the mesh.
Checks:
Check pg missing vias
Check pg drc
Check pg connectivity

## Slide 10
PLACEMENT
Place the standard cells inside the core area
Timing Analysis/congestion Analysis
Legaliazation of standard cell
QOR(Quality of Results) → Area,Power,Timing
Optimaztion

## Slide 11
Checks after placement
Timing – check the setup timing
Congestion- cell density,Pin density
Legality issues
Utilization
Area
MV Violations
DRV – Max Capictance,Max Fan out,Max Transistion

## Slide 12
CTS(CLOCK TREE SYNTHESIS)
Clock Tree Synthesis (CTS) is the most critical stage in physical design. It is the process of distributing the clock signal from a single entry point (the clock pin) to every sequential element (flip-flops and registers) in the chip.

## Slide 13
Checks After CTS
Report Clock QOR
Report Global Routing
s

## Slide 14
ROUTING
Routing is the stage where the tool creates the actual physical connections (metal wires) between the placed cells. After CTS, "placed" a design with a balanced clock.

## Slide 15
Checks After Routing
Check Routes
Check LVS
Check Global Timing
Report Utilization
Report Area
Report Design

## Slide 16
      FILLER INSERTION
Filler Cells are non-functional cells that contain only the power and ground rails and the N-well/P-well layers. We insert them during the final stages of the design (usually after routing and before sign-off) to "fill" the empty gaps between standard cells.